## Slide 1: Interpreter Glove
Presented by:
Sherry Ghobrial
Peter Adel Gaber
Ashrakat Ihab

## Slide 2: PROJECT BRIEFING 01 FLOWCHART 02 PROJECT SOFTWARE 03 PROJECT HARDWARE 04 TABLE OF CONTENTS

## Slide 3: PROJECT BREIFING 01.
Introduction and key components

## Slide 4: INTRODUCTION
The wearable device has sensors that run along the four fingers and thumb to recognize each sign language word, phrase, or letter. This project aims to greatly ease communication for those with disabilities.

## Slide 5: ATMEGA32 Flex sensor External EEPROM Fixed resistance TWI KEY components LCD
The microcontroller
to store the signs and corresponding signals
5 flex sensors ranging between 30kΩ- 100kΩ
2*16 LCD 2.6 inches
5 of 36kΩ resistance
To communicate with the external EEPROM

## Slide 6: HAL APPLICATION MCAL Abstraction Layers
Contains the application functions that store, compare and display the signs.
Contains the LCD and EEPROM drivers.
Contains our microcontroller drivers: DIO, ADC, TWI.
Service
Contains the file for BIT-MATH and STD-TYPES.

## Slide 7: FLOWCHART 02.

## Slide 8: Flowchart

## Slide 9: Flowchart

## Slide 10: SOFTWARE 03.
Algorithm and Stored Signs

## Slide 11
U16 array of base add. of each sign signals [15] | U16 Array of base Add. of the 15 Signs names
Address signal 1 | 0x0000
Address signal 2 | 0x0006
Address signal 3 and so on | 0x000f
Address 0x0000 | Y
 | E
 | S
Address 0x0003 | \0
Two arrays to be built in main.c to hold the base addresses of the sign names and corresponding signal values.
In EEPROM, the sign names as strings as illustrated in the table.
After storing, the ADC reads sensor signals which are compared to stored signals.
Once they match, the sign is displayed on the LCD.
Notes: Peace
I love you
You
Good work
I watching you
Poten
Bathroom
That Is awoms
play
No

## Slide 12
Awesome
Peace
Hello
Have a good life
You
Bathroom
Yes
Perfect
Seven
O.K.
No
I do love you
I’m watching you
I love you
Play
15 stored signs are shown below.
The interpreter glove is calibrated according to the user’s hand movements and is recalibrated for different users.

## Slide 13: HARDWARE 04.
Resistance selection and wiring diagram

## Slide 14: Resistance selection
Our flex sensor's resistance varies from 30kΩ, which represents the flat position, to about 100kΩ, which represents the maximum bending.
The green equation represent the voltage diver equation where x is the resistance of the flex sensor and r is the fixed resistance

## Slide 15: Resistance selection
It is necessary to differentiate the voltage divider equation in order to determine the maximum range between v max and v min. then To determine the r, let's set the result to zero. So the best R =34.856KΩ

## Slide 16: Wiring diagram
Do you know what could help you make your point clear?
Lists like this one:
They’re simple
You can organize your ideas clearly
You’ll never forget to buy milk!
And the most important thing: the audience won’t miss the point of your presentation

## Slide 17: LAUNCH

## Slide 18: Project DEMO

## Slide 19: Project DEMO

## Slide 20: THANK YOU